## Slide 1: History of KNX
Foundation: 1990
Under the name ‘EIB Association’
1999
Merger with two other associations (Batibus and EHS)
Goals
+
+
1990
1999
2006

## Slide 2: KNX – International standardization
KNX – a well established technology!
CENELEC
2003: Approval of KNX as EN50090
CEN
2005: Approval of KNX as EN13321-1/2
ISO/IEC
2006: Approval of KNX as ISO/IEC14543-3-1 bis 7
SAC (P.R. China)
2013: Approval of KNX as GB/T 20965
ANSI/ASHRAE
Reference in US ANSI/ASHRAE standard 135

## Slide 3: KNX – Introduction to the technology

## Slide 4: KNX System specification
Supported
Media
TP
PL110
RF
IP
Standard-Protocol
Extended Protocol
System Mode (PC)
Easy Mode (without PC)
‘
‘
S
S
’
’
‘
‘
S
S
’
’
‘
‘
E
E
’
’
‘
‘
E
E
’
’
Controller
Push Button
LTE
Objects with standardized
Data Point Types
Common Logo
Media Coupler
ETS

## Slide 5: Areas of application for the various media
 | Medium | Transmission via | Preferred areas of application
 | Twisted Pair | Separate control cable | New installations Extensive renovations Highest level of transmission reliability
 | Powerline | Existing network (Neutral conductor must be available ) | If no additional control cable can be installed When 230 V cable is available
 | Radio Frequency | Radio line | When no cables can be installed
 | IP | Ethernet/WIFI | In large installations where a fast backbone is needed For communication with mobile devices

## Slide 6: KNX Interworking
Standardized KNX operating systems (“Bus Coupling Units”)
Standardized transmission media
Application module
Application software (in the device or as ETS product data)
Standardized configuration
Realisation/Installation of many functions

## Slide 7: Possible fields of application
Lighting
Blinds & Shutters
Security
Energy Management
HVAC
Monitoring
Remote Control
Metering
Audio/Video Control
White Goods